## Slide 1: C++ Design, Verification and Automatic Conversion to Synthesizable Verilog on a Large Processor

## Slide 2: Outline
The Need For SPEED!
  Evangelical Tirade
Our Experience
  Project Description
  Process
  Results
C++ HDL Advantages and Costs
Plug for C-Level
Q & A

## Slide 3: The Need For SPEED!

## Slide 4: Verification Challenge
ASIC geometry shrinks are CONTINUING to cause the Verification challenge to outstrip the simulation speedup of Verilog and VHDL simulators.

## Slide 5: How to make a living in Verification
Break large chip into 3 - 5 testable blocks
Create a test environment for each block and another environment for the chip top.
Write BFMs to test each DUT
Create elaborate Testplan (huge list of things to test)
Assemble a team on each block and one for the top.
Write lots of tests
Use Code Coverage and/or Code Inspections
Review Testing in all environments
Sign off Chip

## Slide 6: Pain of Multiple Simulation Environments
Time spent writing and debugging BFMs
BFMs find lots of bugs that would not have occurred in the ASIC
Effort to maintain multiple simulation environments
Effort at the end of the Verification phase to review each simulation environment and find out what has been missed
Duplication of effort between teams

## Slide 7: Alternative
Create and maintain only one permanent, chip level or higher, simulation environment which is tailored to the Verification challenge - ignoring the issue of simulation speed.
Create sub-chip level environments for schedule reasons. These will be short lived and are only used to run simple operations through the sub-blocks until they are ready for integration.

## Slide 8: Our Experience

## Slide 9: Piranha Chip Multiprocessor
31
DRAM
L2
0
CPU
0
iL1
dL1
Fill Buffer
MC
0
0
1
31
DRAM
DRAM
DRAM
...
L2
1
CPU
1
iL1
dL1
MC
1
0
1
31
DRAM
DRAM
DRAM
...
L2
7
CPU
7
iL1
dL1
MC
7
0
1
DRAM
DRAM
...
Input
Queue
Output
Queue
Router
Home
Engine
Remote
Engine
I
n
t
e
r
c
o
n
n
e
c
t
L
i
n
k
s
Memory Arrays
System
Control
P
a
c
k
e
t
S
w
i
t
c
h

## Slide 10: Piranha Flow Diagram
Stylized C++
PP-1
ANSI C++
cxx
C++ (cycle based) executable
C++ Simulation
PP-2
C-RTL
System Compiler
Verilog RTL
Synopsys
Verilog Gates
Verilog/C++
Co-Simulation
1000 clks/sec
20 clks/sec
Formal
Verification

## Slide 11: Piranha Design and Verification Process
Single Code Base written in cycle accurate “stylized” C++ RTL
1000 clocks per second with full chip simulation
  Modules test each other. Only two BFMs to create - CPU, DRAM
  Tests written at the highest level (easy to create long random stress tests with lots of “real”, “interesting” interaction)
  Tests can also be written at a lower level by turning off sub-blocks in the test - for lower level control and observability.
C++/Verilog Co-simulation runs the same tests on the Verilog version of modules.

## Slide 12: Our Results
Very few simulation mismatches between the C++ and RTL Verilog or Verilog gate-level netlist.
Synthesized to expected speed.
Redesigns for Timing required no more effort than our Verilog experiences.
Verilog Output was very readable.

## Slide 13: Our Biggest Problem
The initial modules were designed too large for Synopsys Design Compiler. The largest was 6000 lines of C++ (~5000 DFFs). We have been spending most of our porting effort breaking up large modules into smaller chunks that Design Compiler can synthesize in a reasonable amount of time.
  This was not caused by the C++ simulation environment or translation tool. However, adding hierarchy to the design was somewhat more complex than it would have been with Verilog alone. This is due partly to a C++ learning curve and partly to the sequentiality of C++

## Slide 14: C++ HDL Advantages
C++ Features Worth Moving to C++
  50x - 500x simulation speedup over Verilog
  No runtime simulation licenses needed
C++ Features Not Worth Moving to C++ - but nice bonuses
  Structs - can be used to simplify code
  C++ is a powerful Test Language (Forking, Reentrant Tasks, Object Oriented, Sparse Memory Models, etc.) same stuff you can do with VERA, SPECMAN, VERISITY; more powerful than Verilog and VHDL and runs faster.
  Note: C++ HDL will not allow you to hire C++ Software Engineers to design ASICs. Still have to know what a DFF is.

## Slide 15: C++ HDL Costs
Integrated Debugging Environment is Limited and Immature (Debussy, UnderTow, etc.)
Legacy code and Vendor Cores in Verilog slow simulation environment to Verilog speeds.
  We either had to create a C++ model and verify in the top-level simulation environment, or verify in a separate simulation environment, or both.
Code Coverage and Linting tools are not optimized for Hardware uses yet, but they could be ported.

## Slide 16: C++ HDL Costs (cont.)
Lots of ways to mess up (Memory leaks, pointer manipulation, allocation and deallocation, overloading, sequential operation)
C++ support - Due to our homegrown simulation environment we required C++ experts to solve problems. Using 3rd party tools can help, but there will still need to be some in-house C++ expertise needed if you start with a Verilog or VHDL team.

## Slide 17: C-Level Plug
The support from C-Level has been OUTSTANDING. They have become part of our team, have taken ownership of our success, have provided extremely valuable expertise, and have gone the extra mile to provide us with what we needed to get the job done.
The Cycle-C Simulation methodology and coding style were well documented and made the learning curve as short as possible.
The System Compiler translator does a remarkable job of translating C++ to Synthesizable Verilog - that meets a very aggressive timing goal.

## Slide 18: Summary
Simulation Speed-up over Verilog or VHDL in the 2 - 3 orders of magnitude range is possible with cycle accurate C++. This can save significant effort in the Verification of a design IF USED WELL.
Timing and Redesign results are similar to those achieved with a purely Verilog approach.
Cost of using a new, immature design and verification environment are significant. However, these issues are not a hard problem to solve and should be short lived.