## Slide 1: Audit Your Design to Assess and Even Reduce the Amount of Random Testing Needed
by
Dan Joyce
Ray Harlan
Ramon Enriquez
Hewlett-Packard

## Slide 2: Overview
How to Size Simulation Effort
What are Randomly Timed Stimuli?
Design for less Corner Case Testing
Performance Impact?
How to Perform the Audit
Sample Audit
How to Find Corner Case Bugs
Conclusion

## Slide 3: How to Size a Simulation Effort
Directed Testing
  Usually the only part of the Test Plan
Corner Case Testing
  Often neglected in the Test Plan

## Slide 4: Audit to Size Corner Case Testing
This structured Audit can identify designs which are a high risk to Corner Case Bugs. It also sizes the Effort to verify all the Corner Cases in the design.
The audit points out which state machines in the design are the most at risk for Corner Case Bugs or will take the most effort to verify.
These high risk designs can be redesigned to
  Reduce the number of Corner Cases before simulation and
  Reduce the Effort that will be needed to exercise them.

## Slide 5: Overview
How to Size Simulation Effort
What are Randomly Timed Stimuli?
Design for less Corner Case Testing
Performance Impact?
How to Perform the Audit
Sample Audit
How to Find Corner Case Bugs
Conclusion

## Slide 6: Randomly Timed Stimuli
Corner Case Bugs are caused when Randomly Timed Stimuli interacts in the same logic.
Randomly Timed Stimuli are stimuli that exercise the chip but can come at random times relative to each other.
  Example: A Memory Read on one interface and an Interrupt on another interface. If these two events can occur 1 clock apart, or 20, or -5, or any number of clocks apart, they are Randomly Timed Stimuli. If they interact in the same logic, Corner Case bugs can be in that logic and all timing relationships between these two stimuli must be verified.
Randomly Timed Stimuli are NOT the same thing as Asynchronous Signals.

## Slide 7: Example Design with 5 State Machines affected by 4 different Randomly Timed Stimuli
Design
Shemp
State Machine
R = 4
Joe
State Machine
R=2
R=3
R=1
State Machine
R=1
Bad State Machine – large/complex with many
randomly timed inputs
Curly
Moe
Larry

## Slide 8: Example Design State Machine Analysis
Shemp is a very bad state machine from a verification perspective.
  It is large, so it has many corner cases. This means it has many corner cases that must be simulated.
  It is stimulated simultaneously by 4 Randomly Timed Stimuli. This means it will be very hard to exhaustively test and guarantee that all corner cases were simulated.
Curly is significantly better than Shemp. Smaller, and significantly easier to exhaustively test (3 instead of 4 Randomly Timed Stimuli).
Moe and Larry are not corner case problems at all because they are stimulated by only one randomly timed stimulus (simultaneously).
  Even though Larry is much bigger than Shemp it will have no risk to Corner Case bugs where Shemp has a large risk.

## Slide 9: Overview
How to Size Simulation Effort
What are Randomly Timed Stimuli?
Design for less Corner Case Testing
Performance Impact?
How to Perform the Audit
Sample Audit
How to Find Corner Case Bugs
Conclusion

## Slide 10: Design “Up Front” for less corner case risk
Architect your design so less logic is affected simultaneously by Randomly Timed Stimuli.
  Try to isolate as much of the more complex logic from randomly timed events.
  Reduce the propagation of unnecessary Randomly Timed Stimuli.

## Slide 11: Analogy: Asynchronous Interfaces vs. Randomly Timed Stimuli
Corner Case Bugs and Asynchronous Interface Bugs are similar in that they are VERY hard to find in simulation.
Advice:
Design logic affected by Randomly Timed Stimulus the same way you design Asynchronous Interfaces.

## Slide 12
How do we design Asynchronous Interfaces?
  Reduce the # of Async Intf bugs in the first place.
Reduce the amount of logic affected by Async signals.
  Verify by any means cost-effective: code inspect, simulate w/ timing, lint tools, etc.
How should we design for Randomly Timed Stimulus?
  Reduce the # of Corner Case Bugs in the first place.
Reduce the amount of logic affected by 2 or more “Randomly Timed Stimuli”.
  Verify by any means cost-effective: exhaustive testing, random testing, code coverage analysis, code inspection, Semi-Formal Search tools, etc.
Notes: In order
Prefer Exhaustive Testing
Random Testing means Exhaustive Testing is not possible
Code Coverage helps when Exhaustive testing is not possible to tell us if we missed anything obvious in the logic
Code Inspection gets us further – at more cost
Semi Formal Search Tools are new to the scene

## Slide 13: Redesign Examples
Single Point Arbitration
Isolate Random Events, Errors
Logical Firewalls
State Machine Division

## Slide 14: Single Point Arbitration
Interface
Arbiter and
Interface
Controller
Multiple
Requestors
Interface
Interface
Controller
Multiple
Requestors
Arbiter
Notes: Most of the complex control logic is in the Interface controller. By resolving the arbitration in a smaller more simple state machine, the more complex logic see less variability.

## Slide 15: Isolate Random Event Logic
“Master Port”
“Slave Port”
Propagates
Initial Operations
and Aborts
Propagates
Initial Operations only
– Aborts blocked
Collisions Occur
Responds to
Initiated operations
No Collisions
Firewall
State Machines
Notes: Blocking the aborts keeps collisions from occurring in all the logic in the middle.

## Slide 16: Logical Firewalls
Remainder of ASIC
Extra Board
Logic
Remainder of ASIC
Extra Board
Logic
Firewall
Keep the Extra Board Logic signals
separate from the rest of the ASIC if
possible. Understand the Verification cost.
Notes: Understand the cost of propagating the Randomly Timed Inputs from the separate logic.
  Keep separate if possible.

## Slide 17: State Machine Division
State Machine
Must Check for
Pulse in every
State
State Machine
Checks for
level only in one
or two states
SM
Pulse
Detector SM
Other Randomly
Timed Stimuli
Pulse Input
Notes: Signals that are pulsed – only true for a clock – often cause lots of corner cases.
  Do not look for that signal in every state.
  Instead use a pulse detector state machine to hold the value until the more complex state machine clears it. Then only check the level in an idle type state (when the other operation is complete or paused).
  The pulse detector can be made with a Mealy output so that no delay is introduced.

## Slide 18: Overview
How to Size Simulation Effort
What are Randomly Timed Stimuli?
Design for less Corner Case Testing
Performance Impact?
How to Perform the Audit
Sample Audit
How to Find Corner Case Bugs
Conclusion

## Slide 19: Performance Impact?
Some of the Redesign Examples appear to have a negative impact on Performance. But this should not be the case.
  Many redesigns involve dealing with Error Cases. This is because Error Cases are common sources of Randomly Timed Stimuli. But adding a clock of latency to an error handling action will not impact system performance unless the error occurs frequently.
  Mealy State machines can be used for performance critical paths. These allow the performance critical path to have no added latency. Mealy state machines can still shield a complex state machine from sources of Randomly Timed Stimuli.

## Slide 20: Overview
How to Size Simulation Effort
What are Randomly Timed Stimuli?
Design for less Corner Case Testing
Performance Impact?
How to Perform the Audit
Sample Audit
How to Find Corner Case Bugs
Conclusion

## Slide 21: Audit Process
Analyze the design to identify all the Randomly Timed Stimuli.
Identify which State Machines are affected by 2 or more Randomly Timed Stimuli. Determine the number of Randomly Timed Stimuli (RN) that affects each.
Determine a “Size” for each State Machine (SN). All Sizes should add to 1.0 (including SMs with only 1 random stimulus).
Plug the “Size” and “Random Stimuli” numbers SN and RN for each state machine into the equation:
Effort-Risk = S1*(R1-1)2R1 + ... + SN*(RN-1)2RN
Notes: Concept is more important than the Equation

## Slide 22: Overview
How to Size Simulation Effort
What are Randomly Timed Stimuli?
Design for less Corner Case Testing
Performance Impact?
How to Perform the Audit
Sample Audit
How to Find Corner Case Bugs
Conclusion

## Slide 23: Sample Audit
Master
Interface
SMs
Target Path
Interface SM
Target
Interface
SMs
Sample Design
S1=.05
R1=2
S2=.05
R2=2
S3=.05
R3=2
S4=.1
R4=4
S5=.1
R5=2
S6=.05
R6=2
S7=.05
R7=2
S8=.05
R8=2
Arbiter and Host
Path Interface SM
Notes: Note that sizes only add to about 0.5.
All other state machines are not affected by more than one randomly timed stimulus.

## Slide 24: Sample Audit Equation
Effort-Risk = S1*(R1-1)*2R1 + ... + SN*(RN-1)*2RN
Effort-Risk = .05*(2-1)*22 + .05*(2-1)*22 + .05*(2-1)*22 + .1*(4-1)*24 + .1*(2-1)*22 + .05*(2-1)*22 + .05*(2-1)*22 + .05*(2-1)*22
Effort-Risk = .05*1*4 + .05*1*4 + .05*1*4 + .1*3*16 + .1*1*4 + .05*1*4 + .05*1*4 + .05*1*4
Effort-Risk = 0.2 + 0.2 + 0.2 + 4.8 + 0.4 + 0.2 + 0.2 + 0.2
= 6.4 (Over 1.0 – opportunity for redesign)
Notes: Especially high for such a small single threaded design

## Slide 25: Apply “Single Point Arbitration”
Master
Interface
SMs
Arbiter
SM
Target
Interface
SMs
Sample Design
S1=.05
R1=2
S2=.05
R2=2
S3=.05
R3=2
S4=.09
R4=2
S5=.1
R5=2
S6=.05
R6=2
S7=.05
R7=2
S8=.05
R8=2
S4=.02
R4=3
Master Path
Interface SM
Target Path
Interface SM
Notes: Arbiter broken out of the most complex state machine.

## Slide 26: Apply “Isolate Random Event Logic”
Master
Interface
SMs
Arbiter
SM
Target
Interface
SMs
Sample Design
S1=.05
R1=1
S2=.05
R2=1
S3=.05
R3=1
S4=.09
R4=1
S5=.1
R5=1
S6=.05
R6=1
S7=.05
R7=1
S8=.05
R8=1
S4=.02
R4=3
Master Path
Interface SM
Target Path
Interface SM

## Slide 27: New Effort-Risk Calculation
Effort-Risk = S1*(R1-1)*2R1 + ... + SN*(RN-1)*2RN
Effort-Risk = .05*(1-1)*21 + .05*(1-1)*21 + .05*(1-1)*21 + .02*(3-1)*23 + .09*(1-1)*21 + .1*(1-1)*21 + .05*(1-1)*21 + .05*(1-1)*21 + .05*(1-1)*21
Effort-Risk = .05*0*2 + .05*0*2 + .05*0*2 + .02*2*8 + .09*0*2 + .1*0*2 + .05*0*2 + .05*0*2 + .05*0*2
Effort-Risk = 0 + 0 + 0 + 0.32 + 0 + 0 + 0 + 0 + 0
= 0.32 (Much improved)

## Slide 28: Redesign Reduced Risk and Effort
Effort-Risk dropped from 6.4 to 0.32 with 2 redesigns.
Used:
  Single Point Arbitration
    Simple Arbiter State Machine Broken out of the Combination “Arbiter - Master Path Interface” State Machine
  Isolate Random Event Logic
    Master Abort Error Condition Isolated.
Notes: Look where random testing now needs to be done
  Arbiter only

## Slide 29: Overview
How to Size Simulation Effort
What are Randomly Timed Stimuli?
Design for less Corner Case Testing
Performance Impact?
How to Perform the Audit
Sample Audit
How to Find Corner Case Bugs
Conclusion

## Slide 30: Exhaustive Testing is the Goal! When that is not Possible:
Random Testing
Code Coverage Analysis
Assertions
Code Inspection
Semi-Formal Search Tools

## Slide 31: Random Stress Testing
High Level Test Bench
Hand Tweaking of Tests
Overnight (weekend, holiday) Simulation Runs
Large Simulation Farm
  Advantages:
  Uses power of machines to find corner case bugs.
  Disadvantages:
  As designs get bigger, simulation speed gets slower. This raises the cost and reduces the return on Random Testing.
Notes: Good Test Engineers are worth their weight in gold.

## Slide 32: Code Coverage Analysis
Automated Instrumentation
Plus High-Level Hand Inserted Coverage Points
  Tells you when you are not done.
  Does not tell you when you are done.
  Prioritize State Machines
Assertions
Hand Inserted
Provide Visibility
Prefer in-line to avoid code rot
Notes: Code Coverage Priorities: First: State Machine coverage, Second: Line coverage, Third: Sensitized Condition coverage
Code rot is reduced with in-line Coverage points and Assertions

## Slide 33: Code Inspections
Costly – less code to inspect is better
Semi-Formal Search Tools
Find corner cases simulation did not reach
Work on small chunks of logic (50k – 500k gates)
Require rules for interfaces of logic chunks

## Slide 34: Overview
How to Size Simulation Effort
What are Randomly Timed Stimuli?
Design for less Corner Case Testing
Performance Impact?
How to Perform the Audit
Sample Audit
How to Find Corner Case Bugs
Conclusion

## Slide 35: Conclusion
Directed Testing is easy to estimate.
Use this Audit to estimate Corner Case Testing.
This audit identifies designs which are a concern.
This audit points out state machines in the design that are the most at risk.
These high risk designs can be redesigned to reduce the number of Corner Case Bugs in the first place and also reduce the Effort that will be needed to find them.
The audit shows the simulation team which Randomly Timed Stimuli need to be exhaustively simulated.
Where exhaustive simulation is not possible, we showed other methods to find the Corner Case Bugs.

## Slide 36: Questions and Answers