## Slide 1: Focus: The Automatic Generation of Golden Timing Constraints
Ajay J. Daga
Founder & CEO
FishTail Design Automation

## Slide 2: Design Challenges
Functional complexity
  Multi-million gate designs
  Concurrent, geographically dispersed, IP-based design
Clocking complexity
  300MHz & higher clock speeds
  Multiple clock domains
Conflicting requirements
  Meet performance goals, but…
    Minimize power
    Minimize area

## Slide 3: Existing RTL to GDSII Design Flow
Meet Timing
Requirements
Verify & Add
Exceptions
(NO)
GDSII
(YES)
Verify & Add
Exceptions
(NO)
(YES)
Physical
Design
Place and
Route
Meet Timing
Requirements
Logic
Synthesis
Gate-Level
Netlist
Clocks &
Boundary
Constraints
RTL
Design

## Slide 4: Nailing IC Timing Constraints is Painful
Iterative, time-consuming, process
  Constraints remain in a state of flux throughout design flow
Large, manually generated, constraint files are a cause of anxiety during static timing signoff
  Engineers resort to timing accurate gate-level simulation
Unnecessary design optimization because of over-constrained timing paths
  Poor QOR
  Timing closure is tougher than it needs to be
Messy design handoff
  “Hey, is this timing problem real?”

## Slide 5: RTL to GDSII Flow with FishTail
GDSII
Focus
Golden
Timing
Constraints
Place and
Route
Physical
Design
Logic
Synthesis
Gate-Level
Netlist
Clocks &
Boundary
Constraints
RTL
Design
RTL Handoff
Netlist Handoff

## Slide 6: Focus Value Proposition
Reduction in design cycle
  No need to manually specify & verify exceptions to clocking
  No need to resort to timing accurate gate-level simulation
Reduction in timing closure risks
  Fewer iterations to converge on real timing challenges
Reduction in unit costs
  Unnecessary logic optimization is not performed
Plug and play in the design flow
Empower design handoff
  Golden timing constraints are part of the handoff from design to implementation team

## Slide 7: Focus
Focus
Virtual Prototyping
Logic Synthesis
Place & Route
Static Timing
Golden Timing Constraints
SDC Format
create clock -period 2
create_generated_clock
set_false_path -setup
set_false_path -from
set_multicycle_path 2
Design Description
Verilog Synthesizable RTL, .lib
Clock Specification
SDC format
clk500
clk500_inv
clk250
clk125
0
2
4
6
8
10

## Slide 8: False-Path Generation with Focus
always @(posedge clk)
load_src_ac <= ldac || (((ir_dst == 5'h8) && dst_active) && !ag_lda);
assign flag_comp_12fwd = irupt_shadow_pop ? flag_shadow[12] : (ac_wen_reg || irupt_shadow_pop || bx_addr_3e_wen || subtract) ?
load_src_ac[15] : flag[12];
wire cur_max = (flag_comp_15bit ^ flag_comp_12fwd) || flag_comp_14fwd;
wire src_ac = compare ? (load_src_a || cur_max) : load_src_ac;
always @(posedge clk) begin
if (!compare)
ach <= src_ac;
end
set_false_path -from [get_cells spx_control/load_src_ac_reg] \
-through spx_control/flag_comp_12fwd \
-through spx_control/load_src_ac \
-to [get_cells spx_mac/ach_reg[*]]

## Slide 9: Multi-Cycle Path Generation with Focus
always @ (posedge clk) begin
if (!count && !latch_en) begin
r_op_sel <= op_sel;
r_a <= a;
r_b <= b;
if (op_sel)
count <= count + 1;
else
latch_en <= 1'b1;
end
else if (count && !latch_en) begin
latch_en <= 1'b1;
end
end
assign add = r_a + r_b;
assign mul = r_a * r_b;
assign add_mul = r_op_sel ? mul : add;
always @ (posedge clk)
if (latch_en)
x <= add_mul;
set_multicycle_path -through mul \ -to x_reg \ -setup 2
clk
latch_en
add_mul
Add
clk
latch_en
add_mul
Multiply

## Slide 10: Using Focus to Establish Design Modes
CLKA
CLKB
SEL
Common Mode
create_clock –period 10 CLKA
create_clock –period 5 CLKB
set_false_path …
set_multicycle_path …
Mode CLKA
set_case_analysis 1 SEL
set_false_path …
set_multicycle_path …
Mode CLKB
set_case_analysis 0 SEL
set_false_path …
set_multicycle_path …

## Slide 11: Verifying Focus Generated Constraints Automatically
Generate sensitization conditions for each false path definition in a Focus generated SDC file
Verify sensitization conditions
  Manually (examine RTL)
  By converting sensitization conditions into RTL assertions and using simulation/formal verification
False path:
set_false_path -from [get_cells fract_i2f_reg[*]] \ -through u4/exp_fix_div[*]] \ -to ${out_reg[30:0]}
Sensitization condition:
( fpu_op_r3[2] & !fpu_op_r3[1] & u4/op_div )
RTL:
wire op_div = fpu_op[2:0]==3'b011;

## Slide 12: Verifying Focus Generated Constraints Interactively
View sensitization along path segments
report_path -from spx_control/load_src_ac_reg
-through spx_control/load_src_ac
-to spx_mac/ach_reg
Path 1:
Design Object Sensitization Condition
------------- -----------------------
c1_clk(r)
spx_control/load_src_ac_reg ( 1 )
spx_mac/adder_add_result[15:0] ( v7818 ) | ( !v7818 & v7819 )
spx_control/ac_wen_comp ( 1 )
spx_control/load_src_ac ( v7820 )
spx_mac/ach_pre[15:0] ( !v7818 & v7819 )
spx_mac/ach_reg[15:0] ( !v7820 )
c1_clk(r) ( 1 )
Cumulative path sensitization condition = ( 0 )
Boolean Variable Net Name
---------------- --------
v7818 spx_control/subtract
v7819 spx_control/add_to_ac
v7820 spx_control/compare

## Slide 13: Integrating Focus Constraints into Implementation Flows
Focus
filter_sdc
Physical
Synthesis
Critical Endpoints
Golden Timing
Constraints
Automated Approach
Focus
Static
Timing
Exceptions for Endpoint
Failing Endpoint
Interactive Approach

## Slide 14: Application of Focus to Hierarchical IC Design
Block RTL
Block
Interface
Model
Focus
Chip-Level
Design
Chip-Level
Golden
Timing
Constraints
Chip-Level
Implementation
Tools
Chip-Level
Clocks &
Boundary
Constraints
Block
Boundary
Constraints
Block
Implementation
Tools
Focus
Block
Clocks
Timing
Constraints
Block
Golden

## Slide 15: Application of Focus to Customer Designs
 | Design Data |  |  |  | Analysis Data |  |  | 
Design | RTL Lines | NetBus Count | Clocks | Clock Domains | Modes | False Paths | Run Time (min) | Memory (MB)
1 | 66330 | 10289 | 3 | 3 | 1 | 10 | 3 | 332
2 | 86790 | 5809 | 7 | 4 | 3 | 55935 | 294 | 495
3 | 106963 | 10418 | 10 | 4 | 3 | 243 | 57 | 336
4 | 112855 | 25094 | 27 | 13 | 7 | 719 | 226 | 514

## Slide 16: Summary
Automatic generation of golden timing constraints
  Improves design quality
  Reduces design cycle
  Empowers design handoff
Focus is production ready
  Used on designs ranging from 500K to 2M gates
  Designs had hard IP, BIST, multiple design modes, asynchronous clocks, etc.
  Integrated with Magma and Synopsys design flows
Focus customer ship October, 2003
  Support for Verilog design flows on Linux platforms