## Slide 1: Taping out WASSP using MAGMA tool suites
Hari Krishnan Puravankara
VLSI System Business Unit,
WIPRO Technologies, INDIA

## Slide 2: VSBU – Providing end to end solution
Hardware
Solutions
ASIC
System on Chip
Board / FPGA Design
Product Realization Services
System Integration
Reference Design
Product Maintenance
Turnkey silicon manufacturing
Technology
Solutions
Drivers
Middleware
Network Mgmt
Embedded Device
Concept
Silicon
System
Solution

## Slide 3: Phoenix – WIPRO’s PD methodology
Phoenix
Std Cell/ Custom cell library
FABS
Packaging house
EDA tools
SPEC/RTL/ Netlist

## Slide 4: Why Magma ?
First EDA vendor to offer an actual unified data model.
Integrated environment for handling Deep sub micron issues.
Fast turn arround time.
Gain based synthesis methodology and Early Silicon Performance Reports.
Fixed Timing based placement methodology.
Integrating Magma flow with Wipro’s Phoenix Methodology.

## Slide 5: Design Environment
Tools Used
RTL Synthesis : Design Compiler { Synopsys }
Physical Design : Blast Fusion & Blast Noise
Signal Integrity : Celtic { Cadence } & Blast Noise
STA : Prime Time { Synopsys }
Physical Verification : Assura { Cadence }
Machine Configuration
2 CPU Linux Server – 4GB RAM , 8GB Swap Space
Technology Used
    Process : TSMC – 0.13G
Library Vendor : Artisan
Memory Compilers : Artisan
IO library Vendor : Artisan

## Slide 6: WASSP – DA4
Design Function : Multi Scaleable common application ARM based platform.
Gate Count : 600k Instances
Macro Count : 81 Macros
ARM Count : 4
Pin Count : 250 pads
Die Size : 5 x 5 Sq. mm
Max Freq : 166 MHz { 4 clock domains }
Clocking strategy : Multi-frequency , Multi-phase.
Design Topology : Netlist to GDSII
Library Used : 0.13G Artisan’s TSMC Standard Cell Lib.

## Slide 7: Top Level Architecture of WASSP
Multi port Memory Controller
M0 M1 M5 M2 M3 M4
AHB Matrix
S0 S1 S2 S3 S4 S5
Sub-system1
(SS1)
DMAC
Sub-system2
(SS2)
Sub-system3
(SS3)
Sub-system4
(SS4)
Sub-system1
Slave system
MPMC Slave
DMAC Slave
Fast
Slave IO system
I2C
Slow
Slave IO system
SSP
S
C
I
G
P
I
O
Sub-system3
Slave system
AACI (AC-97)
Sub-System4
Slave system
JPEG2K
Compression
Engine
SS2 Slave
SS3 Slave
SS4 Slave
Shared slaves
Common
Memory
(Mail box)
Interrupt
Reg
APB
UART
Additional
slaves
MPMC
AHB Port3

## Slide 8: Implementation issues
Design Complexity
  Extremely timing critical
  Highly Macro intensive – 4 ARM cores , 81 Memory macros
  Critical IO planning requirement
  Stringent clock tree requirement
  High utilization
  Congestion issues
  Complex power requirement
  Full design closure including SI and Power
Duration : 1.5 months

## Slide 9: PD Flow in Magma Environment
Clock and Timing
Specification,
Netlist
Unsizing Cells
Logic Mapping
Area Optimization
Floor Plan Import/
Generation
Logic Restructuring
Generate core, create elements, place macros, route power.
Initial Cell
Placement
Buffering
Area Optimization
Logic Restructuring
Area Optimization
Cloning
Cell Placement refinement & scan chain optimization
Buffering
Buffering
Pin Swapping
First global routing
Clock Insertion
Sizing
Hold Buffering
Pin swapping
Power Jog Routing
Stub Routing
Slew Fixing
Noise Fixing
Track Routing
Initial Detail Routing
Resizing
Detail Route Refinement for timing and DRC
Antenna Fixing
High Effort Route Refinement& Noise fix
Shield Routing& Noise Fix
DRC/LVS fixing and refinement
3D BA & final timing checks
GDSII Genertaion
Library & Noise Preparation
Simplex Fire&Ice Based 3D extraction and BA for RC verification
Prime time based STA and verification
Assura/Calibre based Physical verification
Celtic Based SI verification
Voltage Storm/
Power Analyzer based power analysis and verification
Power Analysis & Refinment
Power Analysis & Refinment
Power Analysis &Refinment
inputs
Gain based synthesis and mapping
Floor Plan & power plan
Placement , optimization ,detailed power analysis and Groute
Clk insertion & optimization
Final route , SI correction, DRC,LVS and antenna fix, design closure
ECO

## Slide 10: Design Volcano Preparation
IO Views
Standard Cell Volcano
Macro Views
Design Lib Volcano Prep
Library Checks and Validation
Hidden Cells
Dominated Cells

## Slide 11: Pre-Placement Optimization
Good netlist and constraint validation process.
Good understanding of timing using ESP &
timing reports.
Innovative Slack Balancing techniques.
Effective buffer removal on the data path.
Effective load balancing on high fan-out nets.
Netlist Checks
Constraint Checks
Supercell based Optimization
Timing Reports
Physical Binding

## Slide 12: Floorplanning and Powerplanning
Die Size : 5x5 mmsq
Chip Power : 1.2W
Total IO Pad : 250
Bond Pad can be placed with IO pads.
Script based floor plan creation.
DEF based floor plan flow supported.
Versatile blockage declaration styles.
Power2 based flow.
Ring and strap based power routing for macros.
IO to IO power routing feature supported.
Opens, shorts and DRC checks can be performed on the power routes.

## Slide 13: Placement and Legalization
Clock tree constraints defined here.
Super cell based optimization and legalization.
Coarse and Global placement supported.
Detailed congestion analysis supported.
Timing convergence can be accurately predicted.
Versatile placement clustering support available.
Effective post placement optimization.

## Slide 14: CTS and Optimization
Pre routes clock tree.
Super cells based clock tree synthesis supported.
Crosstalk prevention in clock nets.
Useful skew feature can be used.
Versatile clock tree techniques.
Clock net routing is customizable.
Effective post clock tree based buffer
fixing.
Incremental timing correction
supported.
Split cell concept useful.

## Slide 15: Final route and DRC/LVS
SI aware final routing.
Jog routing on power nets is a useful feature.
Shield and space routing techniques available for Xtalk prevention
Wide metal routing prevents signal net EM issues.
Antenna issues can be tackled while routing.
The tile width feature enables effective routing control.
Excellent routing refinements including area based refinement
Metal filler insertion supported.
Good top level and area based DRC checks.
Black box level LVS checks supported.
GDSII merge and export features available

## Slide 16: Sign off Verifications
STA – Prime time
With in 1-3% correlation
DRC – Assura
No errors
Antenna – Assura
No errors
LVS – Assura
No block level LVS errors
Extraction – Simplex
Within 2% in STA
Signal Integrity - Celtic
No violation

## Slide 17: Wish List
Routing capability considering Lithographic issues.
CTS should include more options like clock tree preserve, clock tree exclude etc..
Better floor planning capability like gui based floor plan, special bond pad connection etc…
Should have capability to read in parasitic rule files from sign-off tools.
Blast Fusion should have an option to preserve module level hierarchies.
Blast Fusion should have option to do AreaIO-FP based floor plan.