## Slide 1: Stability Analysis of a Complete RTL-to GDS2 Design Flow
Howard A. Landman

## Slide 2: Introduction
This is a written version of a web seminar that I gave for Magma Design Automation on April 30, 2003. Since there is no voice-over, this version contains more detail. It also has more data points for both test cases.
You can see the original web seminar at http://webevents.broadcast.com/cmp/wcs/detail.asp?event_id=5877

## Slide 3: Outline
Purpose & Methodology
Results
  Test Case A - control logic
  Test Case B - CPU core
Conclusions

## Slide 4: Purpose
This study looked at the stability or predictability of Magma's complete RTL to layout flow (Blast RTL + Blast Fusion).
To do this, I reused and extended techniques that I used earlier on synthesis tools.

## Slide 5: Previous studies
In SNUG 1998 I presented a similar study of Synopsys Design Compiler called Visualizing the Behavior of Logic Synthesis Algorithms. (Available on deepchip and elsewhere.) It explains the methodology in detail and even includes code fragments.
Ambit BuildGates studied but not published

## Slide 6: Conclusions from synthesis studies
EDA tools may behave randomly as inputs vary slightly
Randomness can be measured and quantified if many runs are done
Degree of randomness is a useful quality metric for tools (less randomness is better)

## Slide 7: Methodology
Vary delay constraints while keeping RTL etc. constant
Record input Constraint and output Delay and Area
Plot
  D as function of C
  A as function of C
  D vs A (banana curve)

## Slide 8: Methodology (continued)
The basic idea is to test the stability of a tool or design flow by slightly varying one of its input parameters, and looking at how the outputs change.
Here we vary the delay constraints (desired clock period), but other choices are also possible.

## Slide 9: Why should you care?
Want design flow to give predictably good results and not vary wildly every time you tweak something.
Otherwise
  Cannot be sure whether small problems are real or result of tool fluctuation
  May have to iterate to get good result

## Slide 10: Stability != Goodness
Stability is not the same as goodness.
A tool could reliably give bad results; it would then be stable but not good.
However, a very good tool must be stable, or its randomness will prevent it from finding the best solution much of the time.

## Slide 11: Current Study (1)
Magma asked me to perform a stability analysis for their tools - and broadcast the results - before they even knew what I would say!
In an industry that's typically cautious or even fearful of anything like a benchmark, it's highly commendable for a company to be this open.

## Slide 12: Aside on Benchmarks
Some people might be tempted to treat this study as a comparative benchmark of Magma vs. Synopsys. This would be utterly wrong for so many reasons that it would take several foils to list them all. No comparable study of the latest and greatest Synopsys tools has been published. (But it would be interesting to see one, would it not?)

## Slide 13: Current Study (2)
Same kind of analysis, but for a complete RTL to layout flow - Magma BlastRTL and BlastFusion (internal red build of 3.2)
  Synthesis-only results are not as interesting as they used to be - we care about the whole flow
  Physical effects now dominate
  RTL-to-GDS flows are maturing
  Tools are fast enough to allow many runs on small to medium modules

## Slide 14: Current Study (3)
Included automated steps like:
  scan insertion, stitching, reordering
  clock tree, hold time fixes, ''useful skew''
  spare cells
Left out manual steps (e.g. DRC fixes)
Also left out xtalk / signal integrity steps
As before, plot relations between constraint, delay, and area.

## Slide 15: Current Study (4)
Flow broken into 3 steps
  Step 0: Read RTL
  Step 1: Apply constraints, synthesize
  Step 2: Load floorplan, place and route
Step 0 run only once (takes 1-3 minutes)
Run times given are for steps 1 and 2 combined on a 2.4 GHz Linux blade

## Slide 16: Test Case A
Staging control logic from a microprocessor
4.7 K to 9.1 K cells in .13 um TSMC library
1.7 to 3.6 nS cycle time
3 layer metal (metal 2 most difficult)
Floorplan scaled with cell area (roughly constant utilization)
Flow includes spare cell insertion
Runtime 7 to 18 minutes

## Slide 17: Plot 1: Delay vs. Constraint
Plots clock period of final laid-out design as a function of the clock period requested in the constraints.
Pink line is where delay = constraint. Below right of line is meeting timing and above left is missing timing.

## Slide 19
Delay is somewhat unpredictable in this range, but we don’t care because we’re meeting timing with a lot of margin.

## Slide 20
Delay is somewhat unpredictable in this range, but we don’t care because we’re meeting timing with a lot of margin.
It’s more stable when timing gets hard to meet. Let’s look at a blowup of that range ...

## Slide 22
Peak-to-peak delay variation about 10% ...

## Slide 23
Peak-to-peak delay variation about 10% ...
… but standard deviation much less. Most results are close to optimal.

## Slide 24: Plot 2: Area vs. Constraint
Plots cell area of final laid-out design as a function of the clock period requested in the constraints.
Fastest result had area 1.02 sq. mm. Any area above that is wasted.

## Slide 26
(area of fastest result)

## Slide 27
Overconstraining the tools causes area to increase with no benefit in speed
(area of fastest result)

## Slide 29
Peak-to-peak area variation: about 7%

## Slide 30
Peak-to-peak area variation: about 7%
but only when severely overconstrained

## Slide 31
Peak-to-peak area variation: about 7%
but only when severely overconstrained
Less under achievable constraints

## Slide 32: Plot 3: Area vs. Delay
Sometimes called ''Banana Curve''
Plots cell area of final laid-out design vs. its delay.
Shows achievable tradeoff between delay and area.

## Slide 34
In this region, spending more area
doesn’t buy anything in delay!

## Slide 35
In this region, can reduce delay at essentially zero cost in area

## Slide 36
Interesting tradeoffs all happen here

## Slide 37
Detail of previous graph

## Slide 38: Conclusions A
Severely overconstraining BlastRTL / BlastFusion is a bad idea!
  Area gets worse, run time gets worse
  Timing does not get better!
Why? I can speculate …
  Working on Total Negative Slack?
  No ''critical range'' limit?
Best to tell the tool the truth

## Slide 39: Test Case B
CPU core with bus and memory interfaces
Multiple clocks & resets, JTAG, BIST, PLL
22.3 K to 41.3 K cells
3.8 to 7.0 nS cycle in NEC 0.10 um library
6 layer metal
Fixed floorplan, not scaled
Includes scan insertion / stitching / reordering
Runtime 54 to 110 minutes

## Slide 40: Plot 1: Delay vs. Constraint
Plots clock period of final laid-out design as a function of the clock period requested in the constraints.
Pink line is where delay = constraint. Below right of line is meeting timing and above left is missing timing.

## Slide 42
Flow meets timing
in this range

## Slide 43
Flow meets timing
in this range
… but sometimes fails to meet timing by a small amount with tighter constraints

## Slide 45
When area gets too large for floorplan,
timing gets bad and P&R may even fail!
(The 2 missing points are failures.)

## Slide 46
In this region, overconstraining by a small amount (1-5%) may help.

## Slide 47: Plot 2: Area vs. Constraint
Plots area of final laid-out design as a function of the clock period requested in the constraints.
Smoothness in lower right is due to not very many data points there.

## Slide 49: Plot 3: Area vs. Delay
Before we look at the last graph, let’s take a break to look at the single most famous image from Japanese ukiyo-e woodblock prints, Hokusai's ''Great Wave''
Note especially the scary top part of the wave where it's breaking.

## Slide 50
Hokusai (1760-1849)
The Great Wave Off Kanagawa

## Slide 51
Delay (nS)
Notice any similarity? :-)

## Slide 52
Running out of room is bad
Delay (nS)

## Slide 53: Conclusions B
Slightly overconstraining BlastRTL / BlastFusion can be a good idea!
  If you are missing timing by a little bit, then tightening constraints may help
  Has chance of working in range of < 5%
  If missing by more, fix your RTL!
Leave yourself enough room!
  If congestion is too high, timing will suffer

## Slide 54: Methodology Notes (1)
Synthesis graphs (in SNUG paper) had a stairstep, Manhattan skyline look. Yet the layout flow graphs are more pointy. Why?
  My guess: layout flow has many more steps and therefore much finer granularity; takes more data points to fully resolve the picture
  Another possibility: tool not deterministic
  Either way, I’m not seeing the exponential speedup mentioned in the SNUG paper.

## Slide 55: Methodology Notes (2)
Need to distinguish predictable from deterministic
  Deterministic: Given exactly identical inputs, will always produce exactly identical results
  Predictable: Given nearly identical inputs, will produce nearly identical results
A tool may be predictable without being deterministic (or vice versa).
Users need predictability, not determinism.

## Slide 56: Methodology Notes (3)
When testing full layout flows, it is not enough to just generate timing constraints. We also need to have a floorplan.
There are different approaches to ''keeping everything the same'' as netlist changes
  Keep floorplan constant
  Scale floorplan to keep cell density constant
Some floorplans are easier to scale than others!

## Slide 57: Summary
Computers and (some) EDA tools are now fast enough that studies involving many complete layouts are feasible.
The Magma design flow gives reasonably consistent results as delay constraints vary.
However, asking it to go much faster than possible will not produce good results.